MATERIAL SAFETY DATA SHEET

Date Prepared:  7-1-11

SECTION 1 – PRODUCT INFORMATION

Distributor:    Swiss Clean, Inc.   	Address:  3650 – 44th St. SE, Kentwood, MI  49512    			Emergency Phone:  1-800-424-9300

Trade Name:  Phoenix Adhesive Remover	Appearance and Odor:   Light colored. Liquid, Hydrocarbon.	Product Type:   Adhesive Remover

## SECTION 2 – INGREDIENTS

| Chemical Name/Common Name | CAS No. | % (Optional) | TLV (Source) | TITLE III, SECT. 313 |
| --- | --- | --- | --- | --- |
| Naphtha (Petroleum), Heavy Alkylate | 64741-65-7 |  |  |  |

## SECTION 3 – PHYSICAL DATA

Boiling Point (°F):  347.0 - 383.0°F	 	Flash Point:  124°F (Tagliabue Closed Cup)	 Explosion/Flammability:  0.6 – 7.0%(V)

Auto-Ignition Temperature: 658.0°		Specific Gravity (H2O=1.0):  0.758 at 60.0°F

Vapor Pressure (mm Hg): 0.07 kPa @68°F 		Vapor Density (Air=1):   5.3  State of aggregation:  Liquid/Solid

Solubility in water:  0.05 g/l Negligible.	 	Evaporation Rate (nBuAc=1):   0.1 (ASTM D 3539)

# SECTION 4 – FIRE AND EXPLOSION HAZARD DATA

Flash Point (T.C.C.):  124° F	Flammable Limits:  0.6 - 7.0%(V)  Auto Ignition Temperature:  658.0°F

Specific Hazards:  Carbon monoxide may be evolved if incomplete combustion occurs.  Will float and can be reignited on surface water.   The vapor is heavier than air, spreads along the ground and distant ignition is possible.

Extinguishing Media:  Foam, water spray or fog.  Dry chemical powder, carbon powder, carbon dioxide, sand or earth may be used for small fires only.  Do not discharge extinguishing waters into the aquatic environment.

Unsuitable Extinguishing Media:  Do not use water in jet.

Protective Equipment for Firefighters:  Wear full protective clothing and self-contained breathing apparatus.

Additional Advice:  Keep adjacent containers cool by spraying with water.

## SECTION 5 – REACTIVITY DATA

Stability:   Stable	under normal conditions of use.

Incompatibility:  Avoid heat, sparks, open flames and other ignition sources and strong oxidizing agents.

Volatile Organic Carbon Content:	100%

Hazardous Decomposition Products:  Thermal decomposition is highly dependant on conditions  A complex mixture of airborne solids, liquids and gasses, including carbon monoxide, carbon dioxide and other organic compounds will be evolved when this material undergoes combustion or thermal or oxidative degradation.

## SECTION 6 – HEALTH HAZARD DATA-

Inhalation:  Vapors expected to be slightly irritating, may include a temporary burning sensation of the nose and throat, coughing and/or difficulty breathing.  	Skin:  May cause moderate irritation to skin.  Repeated exposure may cause skin dryness or cracking, may include a burning sensation, redness, swelling and/or blisters.    Prolonged/repeated contact may cause defatting of the skin which can lead to dermatitis.  	Eye:  Vapors may be irritating to the eye, may include a burning sensation, redness, swelling and/or blurred vision.  	Ingestion:  Harmful; may cause lung damage.    Aspiration into the lungs when swallowed or vomited may cause chemical pneumonitis which can be fatal, may include coughing, choking, wheezing, difficulty in breathing, chest congestion, shortness of breath and/or fever.    	Other:  Possibility of organ system damage from prolonged exposure.  Repeated Dose Toxicity:  Cardiovascular system:  chronic abuse of similar materials has been associated with irregular heart rhythms and cardiac arrest.  Central nervous system:  repeated exposure affects the nervous system.    Pre-existing medical conditions of the following organ(s) of organ system(s) may be aggravated by exposure to this material:  Respiratory system, skin and eyes.  May cause long-term adverse effects in the aquatic environment.

## SECTION 7 – EMERGENCY AND FIRST AID PROCEDURES

Eyes:  Flush eyes with water while holding eyelids open.  Rest eyes for 30 minutes.  If redness, burning, blurred vision or swelling persists, transport to the nearest medical facility for additional treatment.

Skin:  Remove contaminated clothing.  Flush exposed area with water and follow by washing with soap if available.

Inhalation:   Remove to fresh air.  If rapid recovery does not occur, transport to nearest medical facility for additional treatment.

Ingestion:    If swallowed, do not induce vomiting:  transport to nearest medical facility for additional treatment.  If vomiting occurs spontaneously, keep head below hips to prevent aspiration.

Advice to Physician:  Causes central nervous system depression.  Dermatitis may result from prolonged or repeated exposure.  Potential for chemical pheumonitis.  Consider:  gastric lavage with protected airway, administration of activated charcoal.

## SECTION 8 – SPECIAL PROTECTION INFORMATION

Respiratory Protection:  				Ventilation Requirements:   Adequate ventilation

Eye Protection:	Safety Goggles			Protective Gloves: Nitrile, PVC or Rubber Gloves

Other Protective Clothing:  Use protective clothing, safety shoes/boots should be chemical resistant.

## SECTION 9 – SPILL OR LEAK PROCEDURES

Steps to be Taken if Released or Spilled:    Avoid contact with spilled or released material.  Immediately remove all contaminated clothing.  Stop leaks without personal risks.  Remove all possible sources of ignition in the surrounding area.  Use appropriate containment to avoid environmental contamination.  Prevent from spreading or entering drains, ditches or rivers by using sand, earth or to direct it’s flow to a safe location, for example by using fog sprays.  Take precautionary measures against static discharge.  Ensure electrical continuity by bonding and grounding all equipment.  Monitor area with combustible gas indicator.

Waste Disposal Methods:   Transfer by mechanical means to a labeled, sealable container for product recovery or safe disposal.  Allow residues to evaporate or soak up with an appropriate absorbent material and sispose of safely.  Remove contaminated soil and dispose of safely.  Do not flush away residue with water.  Retain as contaminated waste.  Allow residues to evaporate or soak up with an appropriate absorbent material and dispose of safely.

## SECTION 10 – STORAGE AND HANDLING INFORMATION

Precautions to be Taken in Handling and Storage:   Avoid breathing of or contact with material.  Use in well ventilated areas.  Wash thoroughly after handling.  Extinguish any flames.  Do Not Smoke.  Remove ignition sources.  Avoid sparks.  Avoid contact with skin, eyes and clothing.  Electrostatic charges may be generated during pumping.  Electrostatic discharge may cause fire.  Ensure electrical continuity by bonding and grounding all equipment.  Restrict line velocity during pumping in order to avoid generation of electrostatic discharge.  Avoid splash filling.  Do NOT use compressed air for filling, discharging or handling operations.  Keep away from flammables, oxidizing agents and corrosives.  Keep containers closed when not in use.  Drain container thoroughly.  After draining, vent in a safe place away from sparks and fire.  Containers, even those that have been emptied can contain explosive vapors.  Do not cut, drill, grind, weld or perform similar operations on or near containers.

D.O.T.  Classification:    UN 1286 Petroleum distillates, N.O.S. 3 III

The Health hazards given on this Material Safety Data Sheet Apply to this product in it’s concentrated form (as supplied)  and may differ significantly at use dilution.  The signs and symptoms of overexposure apply only to negligence in handling or misuse of the concentrated product and not to the routine exposure of the diluted product under conditions of ordinary use.

HMIS HAZARD RATING

| HEALTH | 1 |
| --- | --- |
| FLAMABILITY | 2 |
| REACTIVITY | 0 |

0=Least, 1=Slight, 2= Moderate, 3=High, 4=Extreme