MATERIAL SAFETY DATA SHEET

Date Prepared: 7-1-11

SECTION 1 – PRODUCT INFORMATION

Distributor:    Swiss Clean, Inc.  	                  			Emergency Phone:  1-800-424-9300

Address:        3650 – 44th St. SE, Kentwood, MI  49512

Trade Name:   Phoenix Classic                                                           	Product Type:  Floor Maintenance

## SECTION 2 – INGREDIENTS

| Chemical Name/Common Name | CAS No. | % (Optional ) | TLV (Source) |
| --- | --- | --- | --- |
| Waxes & Inert Materials |  | 10 - 20 |  |
| Water | 7732-18-5 |  |  |

## Balance – Proprietary	    Non- hazardous 	Below reportable levels

## SECTION 3 – PHYSICAL DATA

Boiling Point (°F):   N/E            Specific Gravity (H2O=1.0): 1.03                 pH:  8.2

Solubility in water:  Complete

Appearance and Odor:  Milky white, citrus odor

## SECTION 4 – FIRE AND EXPLOSION HAZARD DATA

Flash Point (T.C.C.):  N/E        Flammability:  Not flammable.

Extinguishing Method:   Treat for surrounding material.

Special Firefighting Procedures:   Firefighters should wear self-contained breathing apparatus.

## SECTION 5 – REACTIVITY DATA

Stability:  Stable    Incompatible Materials:  Strong oxidizing agents.

Hazardous Decomposition Products:  May include and are not limited to oxides of carbon when heated to decomposition.

## SECTION 6 – HEALTH HAZARD DATA

Primary Routes of Exposure:  Eye, Skin, and Ingestion.

Signs and Symptoms of Overexposure (Acute):  May cause eye & skin irritation.  Harmful if swallowed.  May cause stomach distress, nausea or vomiting.

Signs and Symptoms of Overexposure (Chronic):  Prolonged or repeated exposure to skin can cause drying, defatting and dermatitis.

Medical Conditions Aggravated by Overexposure: None known.

No hazardous or carcinogenic components at concentrations requiring reporting under OSHA 1910.1200.

## SECTION 7 – EMERGENCY AND FIRST AID PROCEDURES

Eyes:  Flush eyes with cool water.  Remove contact lenses if applicable and continue flushing for 15 minutes.  If irritation persists, obtain medical attention.

Skin:  Flush with cool water.  Wash thoroughly with soap and water.  Obtain medical attention if irritation persists.

Ingestion:  Do not induce vomiting.  Never give anything by mouth if victim is unconscious, is rapidly losing consciousness or is convulsing.

Inhalation:  Not a normal route of exposure.  If symptoms develop, move victim to fresh air.  If symptoms persist, obtain medical attention.

## SECTION 8 – SPECIAL PROTECTION INFORMATION

Respiratory Protection:  General ventilation is normally adequate.

Ventilation Requirements:  Ensure good ventilation.                               Eye protection:  Safety glasses.

Protective Gloves:  Impervious.  Confirm with a reputable supplier.       Other Protective Clothing:  As required by employer code.

## SECTION 9 – SPILL OR LEAK PROCEDURES

Steps to be Taken if Released or Spilled:  Before attempting clean up, refer to hazard data given above.  Small spills may be absorbed with non-reactive absorbent and placed in suitable, covered, labeled containers.  Prevent large spills from entering sewers or waterways.  Contact emergency services and supplier for advice.

Waste Disposal Methods:  For large quantities, review federal, state/provincial and local government requirements for disposal.

## SECTION 10 – STORAGE AND HANDLING INFORMATION

Precautions to be Taken in Handling and Storage:  Keep out of reach of children.  Store in closed container away from incompatible materials.

D.O.T. Classification:   Not Regulated

The Health hazards given on this Material Safety Data Sheet Apply to this product in it’s concentrated form (as supplied)  and may differ significantly at use dilution.  The signs and symptoms of overexposure apply only to negligence in handling or misuse of the concentrated product and not to the routine exposure of the diluted product under conditions of ordinary use.

HMIS HAZARD RATING

| HEALTH | 1 |
| --- | --- |
| FLAMABILITY | 0 |
| REACTIVITY | 0 |
| PERSONAL PROTECTION | B |

0 = Least, 1 = Slight, 2 = Moderate, 3 = High, 4 =  Extreme