MATERIAL SAFETY DATA SHEET

Date Prepared:  7-01-11

SECTION 1 – PRODUCT INFORMATION

Distributor:    Swiss Clean, Inc.          		             		Emergency Phone:  1-800-424-9300

Address:        3650 – 44th St. SE, Kentwood, MI  49512

Trade Name:  Phoenix Quik-Strip	                                                         	Product Type:   Floor Stripper

## SECTION 2 – INGREDIENTS

| Chemical Name/Common Name | CAS No. | % (Optional) | TLV (Source) |
| --- | --- | --- | --- |
| Ethylene Glycol Monobutyl Ether | 111-76-2 | <10% | 25 ppm (skin/TWA) |
| Silicic Acid – Sodium Salt | 1344-09-8 |  | 2 MG/M3 (as NaOH) |

## SARA HAZARD:  TITLE III, SECTION 313:  Contains the Glycol Ether indicated at less than or equal to 5% by weight.

## SECTION 3 – PHYSICAL DATA

Boiling Point (°F):  212°F		 Specific Gravity (H2O=1.0):  1.016 ±0.005	  	pH:  12.8 ±0.5

Vapor Pressure (mm Hg):  Not Determined		  Vapor Density (Air=1):   Not Determined

Solubility in water:  Complete                                        Evaporation Rate (vs. H2O):    About the same

Appearance and Odor:   Clear, colorless liquid with no distinct odor.

# SECTION 4 – FIRE AND EXPLOSION HAZARD DATA

Flash Point (T.C.C.):  None to boiling	  Flammable Limits:   N/A

Extinguishing Method:   Water Spray (Fog); Dry Chemical; CO2; Foam

Special Firefighting Procedures:  Do not enter confined fire spaces without protective clothing and self-contained air supply.

Unusual Fire and Explosion Hazards:  None

## SECTION 5 – REACTIVITY DATA

Stability:  Stable  		Incompatibility:   Strong acids/oxidizers.  Do not mix with chlorinated detergents (bleach).

Hazardous Decomposition Products:   Burning may produce carbon monoxide and/or carbon dioxide.

## SECTION 6 – HEALTH HAZARD DATA

Primary Routes of Exposure:  Eye, Skin, and Oral

Signs and Symptoms of Overexposure (Acute):  Prolonged or repeated contact of concentrated product with skin and/or eyes will cause irritation and reddening.  Eye damage possible if contact is prolonged.  Harmful or fatal if swallowed.

Signs and Symptoms of Overexposure (Chronic):  Contains material which penetrates skin readily.  Ingestion, prolonged or widespread contact may result in the absorption of potentially harmful amounts.

Medical Conditions Aggravated by Overexposure:  An existing dermatitis.

Carcinogen or Suspect Carcinogen Ingredients:   None

## SECTION 7 – EMERGENCY AND FIRST AID PROCEDURES

Eyes:  Flush eyes with water for at least 15 minutes and call a physician immediately.

Skin:  Wash affected areas with large amounts of soap and water.  If irritation persists, call a physician.

Ingestion:  Do NOT induce vomiting.  Dilute by drinking water.  Call a physician immediately.

Inhalation:  Remove to fresh air.  Start artificial respiration if necessary.  Oxygen may be administered.  Call a physician.

## SECTION 8 – SPECIAL PROTECTION INFORMATION

Respiratory Protection:  Not required under normal use conditions.  Avoid misting conditions.

Ventilation Requirements:  Other	    Eye Protection:  Safety Glasses/Goggles       Protective Gloves:  Rubber/PVC

Other Protective Clothing:  Work clothing covering arms and legs as required to minimize contact.

## SECTION 9 – SPILL OR LEAK PROCEDURES

Steps to be Taken if Released or Spilled:  Safely stop spill at source.  Contain spill by diking with soil or other inert material and CAREFULLY neutralize with dilute acid.  Mop, pump or absorb with inert material and reclaim into sound containers for proper disposal.

Waste Disposal Methods:  Dispose of in an approved waste facility according to Federal, State and Local regulations.

## SECTION 10 – STORAGE AND HANDLING INFORMATION

Precautions to be Taken in Handling and Storage:   No special requirements if product is handled according to good manufacturing practices.  Wash thoroughly after handling.

The Health hazards given on this Material Safety Data Sheet Apply to this product in it’s concentrated form (as supplied)  and may differ significantly at use dilution.  The signs and symptoms of overexposure apply only to negligence in handling or misuse of the concentrated product and not to the routine exposure of the diluted product under conditions of ordinary use.

HMIS HAZARD RATING

| HEALTH | 2 |
| --- | --- |
| FLAMABILITY | 0 |
| REACTIVITY | 0 |
| PERSONAL PROTECTION | x |

0=Least, 1=Slight, 2=Moderate, 3=High, 4=Extreme